## Slide 1
802.11
DEAUTHENTICATION &
EVIL TWIN ATTACKS
How they work — and how to stop them
CYBERSECURITY
802.11
WIRELESS
Cybersecurity Course Project | NMIMS Indore

## Slide 2
THE FOUNDATIONAL FLAW
802.11 Management Frames — Signed or Unsigned?
What are Management Frames?
Wi-Fi communication is split into three frame types:
Data Frames — carry actual traffic (websites, videos, etc.)
Control Frames — low-level channel management
Management Frames — connection lifecycle (associate, probe, authenticate, DEAUTHENTICATE)
The critical flaw:
In 802.11 (up to WPA2), management frames carry NO cryptographic signature. There is nothing preventing anyone from forging them.
A Deauthentication frame is simply the router saying to a client: "you are disconnected." Since it's unsigned, anyone can send one.
Deauth Frame Structure
Frame Control
Type: Management / Subtype: 0x0C (Deauth)
Destination MAC
Target client (or FF:FF:FF:FF:FF:FF = broadcast)
Source MAC
Spoofed — copied from real AP's BSSID
BSSID
Also spoofed to match AP
Reason Code
e.g. 0x0007 = 'Class 3 frame from unassoc station'
⚠ No Signature
Nothing to verify who sent this frame

## Slide 3
ATTACK #1
Deauthentication Attack — Attack Flow
1
Monitor Mode
airmon-ng start wlan0
NIC listens to all traffic
2
Passive Scan
airodump-ng wlan0mon
Capture beacon frames
3
Select Targets
Pick AP BSSID
and Client MAC
4
Forge Deauth
Craft frame with
spoofed source MAC
5
Inject Frames
aireplay-ng -0 0
Continuous flood
6
Client Drops
Victim disconnects
Cannot reconnect
Command: sudo aireplay-ng -0 0 -a [AP_BSSID] -c [CLIENT_MAC] wlan0mon

## Slide 4
ATTACK #2
The Evil Twin — A Rogue Access Point
Core Concept
An Evil Twin is a rogue Wi-Fi access point that impersonates a legitimate network by broadcasting the same SSID (network name).
Why it works:
Devices auto-connect to known SSIDs. If two networks have the same name, the device picks the one with the stronger signal. The attacker can boost their radio power to win.
What the attacker gains:
Once connected, the victim's traffic goes through the attacker's AP. This enables:
Traffic interception (MITM)
Captive portal — fake login page harvesting credentials
DNS spoofing — redirect to phishing sites
SSL stripping (if HSTS not enforced)
Real AP vs Evil Twin
REAL AP
SSID: HomeNet Auth: WPA2 Has Internet ✓
VS
EVIL TWIN
SSID: HomeNet Auth: Open/WPA2 No Internet / Proxy
CLIENT DEVICE
Sees two "HomeNet"
Connects to stronger signal →

## Slide 5
ATTACK #2 — FLOW
Evil Twin Attack — Step by Step Flow
1
Clone SSID
ESP8266 configured
with same SSID
2
Broadcast Beacons
Rogue AP advertises
cloned network
3
Deauth Real AP
Force disconnect
from legitimate AP
4
Victim Scans
Disconnected client
searches for networks
5
Auto-Reconnect
Connects to evil twin
(stronger signal)
6
Captive Portal
Fake login page
harvests credentials
ESP8266 Implementation:
Custom firmware flashed on ESP8266 creates a fake SSID matching the original AP. When victims connect, they are served a captive portal replica of the legitimate login page. Any credentials entered are captured and logged by the ESP8266.

## Slide 6
COMBINED ATTACK CHAIN
How Deauth + Evil Twin Work Together
Monitor Mode
airmon-ng start wlan0
Scan Networks
airodump-ng wlan0mon
Deauth Client
aireplay-ng -0 0 -a <BSSID> -c <CLIENT>
Evil Twin AP
ESP8266 broadcasts cloned SSID
Credential Harvest
Victim enters password in captive portal
Attack Impact
→ Victim forcibly disconnected from legitimate AP
→ Device scans and finds evil twin with same SSID
→ Auto-reconnect to rogue AP (stronger signal)
→ Captive portal mimics legitimate login page
→ Credentials captured in plain text
→ Attacker now has Wi-Fi password

## Slide 7
DEFENSES
How to Protect Against These Attacks
802.11w PMF
Protected Management Frames encrypts management frames including deauth packets. Forged frames fail signature verification and are silently dropped — deauth attack becomes impossible.
WPA3-Personal
Mandates PMF by default. Replaces PSK with SAE (Simultaneous Authentication of Equals) preventing offline brute-force attacks on captured handshakes.
VPN
Encrypts all traffic end-to-end. Even if connected to evil twin, attacker sees only ciphertext. Essential for public Wi-Fi usage.
HTTPS + HSTS
Encrypts web traffic and prevents downgrade attacks. Certificate pinning in apps rejects fake certificates from MITM attackers.
Best protection: WPA3 router + PMF-enabled clients + VPN on untrusted networks